## Slide 1: Chapter 2 - Forecasting Fundamentals
  2.1 Fundamental Principles of Forecasting
  2.2 Major Categories of Forecasts
  2.3 Forecast Errors
  2.4 Computer Assistance

## Slide 2: Forecasting Introduction
Forecasting:
  is the starting point for all planning systems
    the actual customer demand
    the expected demand
  is an estimate made for some future period
  is necessary to develop future plans
  This considers that the time it takes to produce an item exceeds the customers expectations for delivery.

## Slide 3: 2.1 Fundamental Principles
Forecasting is a technique for using past experiences to project demand expectations for the future.
  Not a prediction
    a structured projected based on history
  Several types of forecasts
    long range, aggregated models (capacity)
    short range (product demand)

## Slide 4: Principles of Forecasting
Forecasts
  Are almost always wrong
  Are more accurate for groups or families
  Are more accurate for nearer time periods
  Should include an estimate of error
  Are no substitute for calculated demand

## Slide 5: Why Forecast?
  To plan for the future by reducing uncertainty
  To anticipate and manage change
  To increase communication and integration of planning teams
  To anticipate inventory and capacity demands and manage lead times
  To project costs of operations into budgeting processes
  To improve competitiveness and productivity through decreased costs and improved delivery and responsiveness to customer needs

## Slide 6: What Is Riding on the Forecast?
  Investment decisions
  Capital equipment decisions
  Inventory planning
  Capacity planning
  Operations budgets
  Lead-time management

## Slide 7: Planning Horizon and Time Periods
Time Periods (week numbers)
Forecast Length
Short Mid Long
Weeks Months Quarters
1 2 3 4 5 6 7 8 9 10111213 17 21 26 30 34 39 43 47 52 65 78 91 104
Planning
Horizon
2-30

## Slide 8: What Should Be Forecast?
Business plan
Market direction
2 to 10 years
Sales and operations
Product lines and
families
1 to 3 years
Master production
schedule
End item and
option
Months
Forecast
Time Frame
Notes: Business plan (strategic plan)…
…is concerned with overall marketsand the economy
...its purpose is to provide time for long-term projects like capital
…low level of detail
…usually in units, dollars or capacity
…reviewed quarterly or annually
Production plan…
…concerned with manufacturing activity over the next 1 to 3 years
…budgets, labor planning,long leatime items
…usually for groups or families of items rather than specific items
…reviewed monthly
Master production scheduling…
…concerned with production activity from the present to a few months out
…forecasts are made for individual items rather than families
…forecasts and plans are reviewed weekly

## Slide 9: Sources of Demand
Demand can come from many sources:
  Consumers
  Customers
  Dealers
  Distributors
  Intercompany
  Service parts

## Slide 10: Decomposition of Data
2-33
  Purify the data
  Adjust the data
  Take out the baseline
  Identify demand components
    Trend
    Seasonality
    Nonannual cycle
    Random error
  Measure the random error
  Project the series
  Recompose

## Slide 11: Data Issues for Forecasting
  Availability of data
  Consistency of data
  Amount of history required
  Forecast frequency
  Frequency of model reevaluation
  Cost and time issues
  Recording true demand
  Order date vs. ship date
  Product units vs. financial units
  Level of aggregation
  Customer partnering
2-29

## Slide 12: 2.1 Fundamental Principles
Forecasts are almost always wrong...
  The issue is not whether it is wrong
  The issue is how wrong will it be
  How do we plan to accommodate the error
    buffer stock
    safety capacity

## Slide 13: 2.1 Fundamental Principles
Forecasts are more accurate for groups or families of items...
  Easier to develop a forecast for a product line rather than an individual item within in
    MP3 market v. blue or white MP3
  Individual errors cancel each other out as they are aggregated
    more blue sold than white

## Slide 14: 2.1 Fundamental Principles
Forecasts are more accurate for nearer time periods (shorter periods)...
  Fewer disruptions in near period to impact product demand
  Future period demand is usually less reliable
    predict weather today v. late February

## Slide 15: 2.1 Fundamental Principles
Every forecast should include an estimate of error...
  First principle is how wrong is the forecast
Forecasts are no substitute for calculated demand...
  Always use real data when available

## Slide 16: 2.2 Major Categories of Forecasts
  Two types of forecasts:
  Qualitative
  Quantitative
    time series
    causal
  Primary focus of this chapter is quantitative forecasting.

## Slide 17: 2.2 Qualitative Forecasting
  Generated from information that does not have a well-defined structure
  Are useful when no past data is available
    introduction of new product line
    no sales history

## Slide 18: 2.2 Qualitative Forecasting
  Are based on intuition, informed opinion, or some external qualitative data
  Tend to be subjective
    developed (biased) from the experience of the forecaster developing them
      can be pessimistic or optimistic
  Allows for rapid forecating
  May be only method available
  Used for individual products, not markets

## Slide 19: Qualitative Forecasting
  Are used for business planning and forecasting for new products
  Are used for medium-term to long-term forecasting
  Common methods include:
    Market surveys
    Delphi or panel consensus
    Life cycle analogies
    Informed judgement

## Slide 20: 2.1 Qualitative Forecasting
  Market surveys
    structured questionnaires given to potential customers
    solicit opinions about products or potentials
    effective for short term forecasting
      if administered properly
      if analyzed properly
    drawbacks include:
      expensive
      time-consuming

## Slide 21: 2.1 Qualitative Forecasting
  Delphi or panel consensus...
    Uses a panel of experts in the market area of interest
    These experts use their experience and knowledge of market issues to forecast and develop a consensus
    Panel consensus brings experts together for a consensus
    Delphi brings individual forecasts together for analysis
    Expensive, but accurate

## Slide 22: 2.1 Qualitative Forecasting
  Life cycle analogy...
    Used when product or service is new
    Assumes most products have a fairly defined life cycle
      growth during early stage
      little growth during maturity stage
      decline during latter stage
    What is the time frame?
    How rapid will growth be?
    How large will the demand be during maturity?

## Slide 23: 2.1 Qualitative Forecasting
  Informed judgement...
    Quite common to use
    One of the worst methods to use
    Example:
      each salesperson develops own forecast
      sales manager combines individual forecasts
    Some are too optimistic
    Some will consider the forecast a quota
    Some will be negatively or positively influenced by recent events
      higher or lower sales

## Slide 24: 2.1 Anecdotal Example
  Joe receives sales forecast...
    10,000 units of product X sold last few years
    product X was sold to 6 user companies
    the forecast is for 16,000 units of product X to be sold in the coming year
      no new customers
      no new uses by existing customers
      no new expansion plans by existing customers
      no new expansion plans by customers of product X
      just because

## Slide 25: 2.1 Anecdotal Example
  What should Joe plan to make?
    Some steel is very long lead time material
    make 16,000 with demand 16,000…good
    make 16,000 with demand at 10,000…bad
      expensive inventory left on hand
    make 10,000 with demand at 10,000…good
    make 10,000 with demand at 16,000…bad
    Correct answer is make 10,000 units.

## Slide 26: General Methods of Forecasting
  Qualitative—based on intuitive or judgmental evaluation
  Quantitative—based on computational projection of a numeric relationship
  Intrinsic—based on historical patterns of the data itself from company data
  Extrinsic—based on external patterns from information outside the company

## Slide 27: 2.1 Quantitative Forecasting - Causal
  Causal forecasting key characteristics...
    Based on concept that one variable causes another
    Assumes causal variables can be measured
      leading indicators
    When accurate leading indicators are developed, they produce excellent results
    Development of the causal models educates the forecaster to other elements of the market
    Causal methods are typically used for markets
    Time consuming and expensive to develop

## Slide 28: Leading Indicators
Indicator
Housing starts
Number of babies
Hits on a Web site
Health trends
Healthier lifestyle
Influences volume of
Building materials
Baby products
e-commerce sales
Medical supplies
Nutritional products
Fitness products
2-26

## Slide 29: Economic Cycle

## Slide 30: 2.1 Quantitative Forecasting - Causal
  Input-output models
    large and complex models
    examine flow of goods and services in the entire economy
    expensive to gather large volumes of data
    used to project needs of entire markets, not specific products
  Econometric models
    statistical analysis of various sectors of the economy

## Slide 31: 2.1 Quantitative Forecasting - Causal
  Simulation models
    use of computers for simulations
    require large data gathering
    are fast and economical
      once data has populated the model
  Regression analysis
    a statistical method to define analytical relationships between two or more variables
    the independent or causal variable is the leading indicator
    Causal forecasts are called extrinsic forecasts.

## Slide 32: External (Extrinsic) Factors
  New customers
  Plans of major customers
  Government policies
  Regulatory concerns
  Economic conditions
  Environmental issues
  Global trends
2-25

## Slide 33: Factors Influencing Demand
Major factors influencing demand...
  General business and economic conditions
  Competitive factors
  Market trends
  Firm’s own plans…advertising, promotions, pricing, product changes
____________________
____________________

## Slide 34: 2.1 Quantitative F’cstg - Time Series
  Commonly used
  Assumes past is valid indicator of future
  Only real variable is time
  Are popular with operations managers
    they have little knowledge of external markets
    used to make production plans
    previous demand is typically readily available
    Quantitative forecasts are based in internal data and are sometimes called intrinsic forecasts.

## Slide 35: Internal (Intrinsic) Factors
  Product life-cycle management
  Planned price changes
  Changes in the sales force
  Resource constraints
  Marketing and sales promotion
  Advertising
2-24

## Slide 36: Demand Patterns
  Dependent versus independent
  Only independent demand needs to be forecast
  Dependent demand should never be forecast

## Slide 37: Demand Patterns
  Stable versus dynamic
  Stable demand retains same general shape over time
  Dynamic demand tends to be erratic

## Slide 38: Characteristics of Demand

## Slide 39: Sources of Demand
Let’s look at demand.
All sources of demand must be identified:
  Customers
  Spare parts
  Promotions
  Intracompany
  Other

## Slide 40: 2.1 Quantitative F’cstg - Time Series
  Most time series forecasts capture underlying patterns of past demand
  Random patterns
    assumes patterns are random
    assumes customers do not demand products and services in a uniform and predictable manner
    require some smoothing forecast method
  Trend patterns
    can be increasing or decreasing, linear or non
    might be more easily forecast (up or down)

## Slide 41: 2.1 Quantitative F’cstg - Time Series
  Seasonal pattern
    sometimes associated with seasons
      summer gear
      winter equipment
    are better defined as cyclical patterns
      pattern of food sales at a restaurant
        breakfast, lunch, dinner
        bread sales in a grocery store

## Slide 42: Seasonality
  Measures the amount of seasonal variation of demand for a product
  Relates the average demand in a particular period to the average demand for all periods
2-20

## Slide 43: Developing A Seasonal Sales Index
Quarter Average Quarterly Sales/100 Seasonal Index
1 128/100 = 1.28
2 102/100 = 1.02
3 75/100 = 0.75
4 95/100 = 0.95
Total = 4.00
2-21

## Slide 44: Seasonality

## Slide 45: Seasonal Sales
Average Sales
for All Periods
2-22

## Slide 46: Data Preparation and Collection
  Record data in terms needed for the forecast
  Record circumstances relating to the data
  Record demand separately for different customer groups

## Slide 47: Intrinsic Quantitative Techniques
Month
Sales
January
92
February
83
March
66
April
74
May
75
June
84
July
84
August
81
September
75
October
63
November
91
December
84
January
?

## Slide 48: Moving Averages
Forecast sales as an average of past months
An average of the past 3 months:
If January sales are 90, forecast for February

## Slide 49: Moving Average Forecasting
  It can be used to filter out random variation
  Longer periods smooth out random variation
  If a trend exists, it is hard to detect
    steel consumption, 12,000 MT v. 23,000 MT
  Manual calculations can be cumbersome when dealing with more periods

## Slide 50: Moving Average Forecasting
Advantages
  A simple technique that is easy to calculate
  It can be used to filter out random variation
  Longer periods provide more smoothing
Limitations
  If a trend exists, it is hard to detect
  Moving averages lag trends
2-20
Notes: This slide lists some of the uses and limitations of moving average forecasting:-
The moving average is a very simple forecasting technique which lends itself to manual calculation.
An advantage of moving averages is that they are a good way to filter out random variation from a demand series. The longer periods the more smoothing occurs. This means that a monthly forecast would have more smoothing than a weekly forecast which would be smoother than a daily forecast.
A limitation for moving average forecasts is that they do not detect or react to trends very well. By the very nature of calculation a moving average will lag any trends and hence this method of forecasting is not good for products subject to seasonal or dynamic changes in demand.

## Slide 51: Figure 2.5 - A Three-Period MA
  Forecast line is smoother than the actual demand line
    the more periods used, the smoother the forecast line
      less responsive to actual demand trend
    the fewer periods used, the more erratic the forecast line
      less responsive to actual demand
    the forecast lags actual demand

## Slide 52: Figure 2.6 - Trend Analysis
  Forecast line lags the demand line
  What are the implications of this if it is depicting the sale of a new product?

## Slide 53: 3 Period Moving Average
What is the forecast for period 4 through 12?

## Slide 54: 3 Period Moving Average

## Slide 55: Moving Average Graph

## Slide 56: 3 Period Moving Average

## Slide 57: Weighted Moving Average Graph

## Slide 58: Weighted Moving Averages
  Same as moving average forecast
  Forecast line lags the demand line, but some intelligence is added to improve the accuracy
  A weight is added by the forecaster to help add more weight to some periods over others

## Slide 59: Weighted Moving Average

## Slide 60: Weighted Moving Average

## Slide 61: Weighted Moving Average

## Slide 62: Exponential Smoothing
New Forecast = a (Actual Demand) + (1-a)(Old Forecast)
  Provides a routine method of updating item forecasts
  Exponent is a weighting factor applied to the demand element
  Works well for items with fairly constant demand Is satisfactory for short-range forecasts
  Detects trends, but lags them
2-21
Notes: Exponential smoothing is a form of moving average forecasting which uses weighting factors to modify the emphasis placed on more recent time periods.
Exponential smoothing uses a weighting factor called alpha which is expressed as a decimal quantity. This factor is used to weight the most recent past period, with the reciprocal being used to weight the more distant past period.
It is not necessary to explain the exponential smoothing formula in this course, but the key concepts of exponential smoothing should be covered.
Exponential smoothing works well with items that are subject to stable demand, I.e no seasonality or trend components.
Exponential smoothing is good for short range forecasts, and it can detect trends, but like any moving average program it lags the trend.
Explain that an extension of this method is called double exponential smoothing and this requires the use of two weighting factors, alpha and beta, and the purpose of this technique is to respond

## Slide 63: Exponential Smoothing

## Slide 64: Exponential Smoothing

## Slide 65: Exponential Smoothing

## Slide 66: Exponential Smoothing

## Slide 67: Tracking the Forecast
  Forecasts are rarely 100% correct over time.
  Why track the forecast?
  To plan around the error in the future
  To measure actual demand versus forecasts
  To improve our forecasting methods
2-23

## Slide 68: Forecasts Can Be Wrong in Two Ways (cont.)
Random variation: Sales will vary plus and minus about the average.
There is no bias, but there is random variation each month.
2-25

## Slide 69: Problem 2.3 (Solution)
2-27

## Slide 70: Choice of Exponential Smoothing Factors
0.1 Low weighting -most smoothing
0.9 High weighting - close to actual
Actual sales
2-22

## Slide 71: 2.3 Forecast Errors
  Every forecast should contain two elements…
    the forecast
    an estimate of its error
  Remember the forecast is almost always wrong
    use of buffer stock or capacity is used to compensate for this error
  Calculations can be used to calculate the error

## Slide 72: 2.3 Mean Forecast Error (MFE)
  Is a mathematical average of the forecast error over some period of time
  The difference between the forecast and the actual demand is called forecast error
  MFE sums all errors and divides them by the total of all forecast errors
  If positive, then demand was greater
  If negative, then demand was lesser
  Is also called bias
    zero is no bias

## Slide 73: 2.13 - Mean Forecast Error
What is the MFE? Is there bias?

## Slide 74: 2.13 - Mean Forecast Error

## Slide 75: 2.3 Mean Absolute Deviation (MAD)
  Is a mathematical average of the absolute forecast deviations
  Indicates the average forecast error
    is always positive
  Is also called bias

## Slide 76: 2.14 - Calculation of Absolute Errors
What is the MAD?

## Slide 77: 2.14 - Calculation of Absolute Errors

## Slide 78: 2.3 Tracking Signal
  Is similar to control limits used in SPC
  It helps one control the forecast by taking actions at some established point
    tracking signals
  running sum of errors / MAD = tracking signal
  It has no ratio or value, but is merely used as a subjective signal

## Slide 79: 2.14 - Calculation of Tracking Error

## Slide 80: 2.4 Computer Assistance
  Speed, reliability and relatively low cost allow for computerized modeling
    take actuals and compare with different model results
    perform simulations
    seek lowest MAD
    must be cognizant of outliers

## Slide 81: Dealing with Outliers
X
500
2-32

## Slide 82: Design Issues of the Forecast System
  Determine information that needs to be forecasted
  Assign responsibility for the forecast
  Set up forecast system parameters
  Select forecasting models and techniques
  Collect data
  Test models
  Record actual demand
  Report accuracy
  Determine root cause of variance
  Review forecasting system for improved performance

## Slide 83: Pyramid Forecasting
SKU by Customer by Location
SKU by Customer
Stockkeeping Unit (SKU)
Package Size
Model/Brand
Product Subfamily
Product Family
Business
Unit
Total
Company
Roll up
Actual
Demand
Force
down
Forecasts

## Slide 84: Technique—Pyramid Forecasting
Total company:
Business unit:
Product family:
Subfamily:
Model/brand:
Package:
SKU:
SKU by customer:
SKU by cust.
by location:
Sales Forecast
SuperNet
Voice, data, media
Large business unit, small business unit, residential business unit
Encryption, storage, routers
Alpha, beta, gamma
Fiber, microwave
1210, 1220, 1230, 1240
1210 for customer 12456
1210 for customer 12456, location 4

## Slide 85: Data Preparation and Collection
  Record sales data in same periods as forecast data
  Daily, weekly, or monthly
  Track sales, not shipments
  Record the circumstances of exceptional demand
  Record demand separately for unique customer groupings and market sectors
2-31
Notes: One of the important aspects of forecasting is how the data is collected and recorded. The data should be collected in the same terms as the forecast is required. For example if the forecast is required to be expressed in weekly intervals, then the data should be collected in weekly intervals as well.
It is important to record sales numbers in history not merely shipments. The sales numbers should also include lost sales
One of the concerns in forecasting is the idea of outliers, these are data points that do not fit the regular pattern of sales.
Record information by groups of customers, the groups of customers can be organized by any classification that makes sense, it could be by type of customer, industry, market, demographics etc.

## Slide 86: Homework
  Chapter 1
    Discussion questions 1,3,4,5,8
    due 2/8/07
  Chapter 2
    Discussion question 1
    Problems 1,7
    due 2/8/07